The purpose of this policy is to provide guidelines & standards to maintain and protect the, Fire Facilities Training Tower and associated equipment.

An additional safety assignment shall be required to observe and ensure that the following standards are adhered to. The assignment shall be coined; Facility Safety Officer (FSO) and designated Authority Having Jurisdiction (AHJ).

The FSO shall be the AHJ on all live fire operations involving the “Fire Facilities Training Tower” and corresponding equipment.

- San Diego County Air Pollution Control District permits shall be filed by the FSO or designate 24 hrs prior to live fire training.

- San Diego County Air Pollution Control District air quality levels shall be checked and noted for records by the FSO via: http://www.sdapcd.org/air/forecast/otoday.html

Live fire training shall be permitted if air quality index is moderate to good. Live burns shall be cancelled if air quality index is poor.

- Notifications shall be made per pre-burn notification list by the FSO or designate. See: Live Fire SOP

Required 24 hrs prior notices

  - NBC Environmental

  - NBC PWO

  - NBC Security

Required Day of training notices

  - NBC CDO

  - NBC ODO

  - Region Fire Dispatch

  - NBC Security

  - Battalion 11

  - NBC Navy Lodge

- The FSO shall attend required operational safety brief. The FSO shall brief both trainers and trainees to facility maintenance and protection requirements for day of live fire training and post training procedures.

- The FSO shall work closely with FD supervisors to insure that the training participants cooperate and adhere to procedures.

- Procedures during live fire training, The FSO shall ensure the following live fire training procedures:

  - Site Set-Up & Pre-Burn Checklist shall be adhered to. (see Live Fire SOP)

  - Pretest temperature monitoring equipment.

      - Fixed Fire Facilities monitor. (requires 4 AA batteries)

      - Alternately or in additionally a Thermal Imaging Camera with temp monitor feature can be used.

- Engines designated to pump shall be staged in H20 reclamation area.

- Excessive coupling leaks shall be corrected or located in reclamation area.

6. Continued, procedures during live fire training:

  - The FSO shall wear PPE appropriate for fire ground operations to include a SCBA if entering the trainer during Live Fire Training.

  - The FSO shall have radio communications with the IC & Operational Safety Officer.

  - The FSO shall contact NBC Air Tower prior to prior to AM burn session and PM session.

  - ONLY permit wood pallets or other clean untreated wood, straw, and paper to be used as fuel.

  - Fuel shall be burned in metal containers on metal pallets.

  - The FSO shall insure that building temps are constantly monitored with Thermal Imagining Devices (TICs)

      - Operational ceiling temps shall not exceed 1000 degrees F.

      - Incidental ceiling temps shall not exceed 1200 degrees F.

      - The FSO shall direct interior safety crews to apply water as needed to control temps.

  - The FSO shall insure that the burn rooms are monitored and controlled between live fire training operations.

  - The FSO shall insure that spent fuel and burning debris are disposed of in the designated burn receptacle. Hot coals shall be extinguished and wet.

- Procedures for “Post Live Fire Training”: The FSO shall ensure the following post live fire training procedures:

- All Fuel is removed from building.

  - Spent fuel and burning debris are disposed of in the designated burn receptacle. Hot coals shall be wetted.

  - Unburned combustibles shall not be placed in burn receptacle.

  - Movable walls are arranged in storage area.

  - Smoke machines are cleaned and stored.

  - Power can be turned on as needed for light.

  - Interior is reasonably washed down.

  - Excess water is swept out of the South door

  - Close and latch windows.

  - Wash exterior walls as necessary.

  - Sweep and hose hardscape around building as needed.

  - Drain all water hoses toward grated flute drains

  - Trash and debris shall be disposed into 40 yard dumpster. (Insure no hot coals or debris)

  - Tools and equipment to be returned.

  - A general area clean-up shall occur before crews leave.

The FSO shall be responsible for the requirements of

NFPA 1403 on Live Fire Training:

9.1.1 The following records and reports shall be maintained on all live fire training evolutions in accordance with the requirements of this standard:

- An accounting of the activities conducted.

- A listing of instructors present and their assignments.

- A listing of all other participants.

- Documentation of unusual conditions encountered.

- Any injuries incurred and treatment rendered.

- Any changes or deterioration of the structure.

- Documentation of the condition of the premises and adjacent area at the conclusion of the training exercise.

The Live Fire binder with forms and check off lists shall be maintained by the FSO and returned to the Regional Training Center Office.