PHASE I: SIZE-UP

### Primary Assessment

### Secure witness or competent person

- Identify immediate hazards

- Location, number and condition of victims

- Secure entry permit

###### Secondary Assessment

- Type of space

- Product in space

- Hazards – atmospheric / physical

- Diagram of space

- Structural stability of space

- Proper personnel and equipment on scene

- Rescue or recovery

###### PHASE II: PRE-ENTRY OPERATIONS

###### Make General Safe Area

- Establish perimeter

- Evacuate if necessary

- Traffic / crowd control

###### Make Rescue Area Safe

- Establish “lobby control”

- Utilize accountability system

- Test atmosphere

- Prior to and after opening

- All levels – O2, flammability,

Toxicity and record on permit

- Ventilate

- Secure Hazards – Lock out / Tag out

###### PHASE III: RESCUE OPERATIONS

Action Plan With Back-up Entry Team Ready

- Back-up team in place

Proper Equipment

- Personal protective equipment

- Lighting

- Communications

- Respiratory protection SCBA or SAR Extra air bottles

- Continuous air monitoring by attendant

- Personal air monitor for entrants

- Fall protection / retrieval system

- Rescuer harnesses

Victim Assessment

- Patient Packaging / Extrication devices

###### PHASE IV: TERMINATION

- Personnel accountability

- Remove equipment

- Secure scene

- Debrief (if possible)

###### ADDITIONAL RESOURCES

- Mutual Aid Fire Department

- Haz. Mat

- Law Enforcement

- Public Works

- Additional Personnel

Additional Info: