## Slide 1: Basic Command, IDHA and Action Plans

## Slide 2: ERP/SOG Will Identify Your Role
What position are you assigned to?
Who do you report to?
E-2

## Slide 3: Purpose of ICS
Provide effective coordination at scene
E-2

## Slide 4: Need for ICS
Manage response
Hazmat incidents often cross jurisdictions
OSHA regs require it
E-2

## Slide 5: Benefits of ICS
Standard organization
Coordinated response
Standard roles & responsibilities
E-2

## Slide 6: The IDHA Process
Most critical aspect of a response
  All decisions flow from this
  Regs require IC to do it
  Can’t protect from the problem if you can’t identify the problem!
E-4
Notes: Protect:
Life,
Environment,
Property.
In that order!

## Slide 7: IDHA Process
Starts with initial discovery
Use recognition clues
  And common sense!
Caution!
  Initial reports may be wrong!
E-4

## Slide 8: Basic FRA IDHA Process
Identify material(s)
Consult ERG/SDS
Follow employer’s policies
E-4

## Slide 9: Basic IDHA Questions
Will something bad happen now?
  Is it on fire?
  Can it explode or burn?
  Is there a gas or vapor present?
E-4

## Slide 10: Basic IDHA Questions
Can it hurt me?
  Toxic
  Flammable
  Corrosive
  Radioactive
E-4

## Slide 11: Info Sources to Aid IDHA
Safety Data Sheets
  S.D.S.
E-6

## Slide 12: SDS - Who
Required by OSHA Hazcom Standard
  29 CFR 1910.1200
  Title 8 CCR 5194
E-6

## Slide 13: SDS - Purpose
Informs employees of “hazardous chemicals”
Ensures all chemicals hazards are:
  Evaluated and
  Info is transmitted to employees
E-6

## Slide 14: SDS - How
Transmits info via:
  Haz. Comm. Program
  Container labeling
  MSDS/SDS
  Employee training
E-6

## Slide 15: SDS
Major source of hazmat info
E-6

## Slide 16: SDS Provides Info On…
Physical properties
Hazards of material
Signs & symptoms of exposure
Exposure levels
PPE recommended
Manufacturer contact info
E-6

## Slide 17: Who Can Provide an SDS
Workplace involved
Manufacturer/distributor
CHEMTREC
E-6

## Slide 18: Hazard Identification Sources
DOT placards, labels & markings
E-8

## Slide 19: Hazard Identification Sources
Placards and labels
  Stenciled railcars
E-8

## Slide 20: Hazard Identification Sources
Placards and labels
  ID # on placards & orange panels
E-8

## Slide 21: Hazard Identification Sources
DOT Radioactive labels
  White I (lowest level of activity)
  Yellow II
  Yellow III (highest level of activity)
E-8

## Slide 22
E-8

## Slide 23: Hazard Identification Sources
Shipping papers
“X” marks the spot!
E-8

## Slide 24
Proper Shipping Name
E-8

## Slide 25
Hazard Class
E-8

## Slide 26
ID Number
E-8

## Slide 27: Hazard Identification Sources
Pipeline Markers
  Level of hazard
  Name of product
E-8

## Slide 28: Hazard Assessment Sources

## Slide 29: NFPA 704 System
Blue = Health
Red = Flammability
Yellow = Instability
No color = special hazards
E-10

## Slide 30: Special hazard symbols
COR (corrosive)
POL (polymerization hazard)
OXY (oxygen or oxidizer)
Trefoil (radiation hazard)
W (water reactive)
E-10

## Slide 31: Numerical Rating Scale
0 – 4
  0= no hazard
  4 = highest hazard
E-10

## Slide 32: Pesticides & Consumer Products
Label must include
  Chemical Name
    Consumer products
  Ingredient Statement
    Pesticides
E-10

## Slide 33: Product Label Signal Words
Bad Stuff
Pesticides & Consumer Products
  Danger (highest hazard)
  Warning (moderate hazard)
  Caution (lowest hazard)
E-10

## Slide 35: CHEMTREC
CHEMTREC
  Chemical Transportation Emergency Center
24 Hour technical information center
  (800) 424-9300
E-12

## Slide 36
Can provide
  SDSs (from members companies)
  Access to specialized advice
E-12

## Slide 37: Other Reference Guides
NIOSH Pocket Guide
E-12

## Slide 38: Other Reference Guides
Poison Control System
E-12

## Slide 40: Other Reference Guides
ChemTel, 3E Company, Infotrac
  24 hour info centers
  Provide SDS from member companies
  Dispatch company response teams
Phone numbers are in ERG
E-12

## Slide 41: DOT Emergency Response Guidebook (ERG)
E-14

## Slide 42: ERG Purpose
Basic safety tool
Basic identification
Initial actions
E-14

## Slide 43: ERG versus SDS
ERG – transportation incidents
SDS – all other incidents
  If current version is available!
ERG
SDS
E-14

## Slide 44: ERG Page Colors & Organization
E-14

## Slide 45: ERG White Pages (part 1)
Instructions (page 1)
Safety Precautions (pages 2-3)
Hazard Classes (page 4)
Table of Placards (pages 5-7)
E-14

## Slide 46: ERG White Pages (part 1)
Railcar & Road Trailer ID (pages 8-9)
Intermodal Container ID # (pages 10-13)
Pipeline ID & Info (pages 14-19)
E-14

## Slide 47: ERG Yellow-Bordered Pages
Materials listed by ID number
E-14

## Slide 49: ERG Blue-Bordered Pages
Materials listed by name
E-14

## Slide 51: ERG Orange-Bordered Pages
Number guide pages
E-14

## Slide 53: ERG Green-Bordered Pages
Isolation & Protective Actions
  Toxic Inhalation Hazards
  Water Reactive Substances
  Six Most Common Substances
E-14

## Slide 57: ERG White Pages (part 2)
Response Info
BLEVE Safety Precautions
Glossary
E-14

## Slide 59: ERG—Good But Limited
Classification of hazard
Guides — “most essential guidance”
Isolation/evacuation distances — guides
Use table of placards only if no ID
Intended use
  “initial phase”
E-16

## Slide 60: ERG Specialized Info
“P”: polymerization hazard
Dangerous Water–Reactive Materials
Guide 111
E-16

## Slide 61: ERG Caveats
Distances are guides
Use table of placards if you can’t ID material
Intended use
  Transportation-related incidents
  Initial phase of incident
E-16

## Slide 62: ERG Use
So let’s use it!
ERG

## Slide 63: What Should This Stuff Not Do?
Notes: Guide 148 – Don’t let it warm up.

## Slide 64: What’s This?
Which guide do you use?
Notes: 1649 = Motor fuel anti-knock mixture. Guide 131

## Slide 65: What are the hazards?
Notes: Toxic (very) and Flammable (highly)

## Slide 66: What’s the Initial Isolation Distance?
Notes: 200 feet. Table 3. It’s an agricultural nurse tank.

## Slide 67: What Guide Page?
Notes: Page 5 of the ERG: “If multiple placards point to more than one guide, initially use the most conservative guide(i.e., the guide requiring the greatest degree of protective actions).” In this case, that would be the Flammable placard.

## Slide 68: What if it Gets Wet?
Notes: Table 2 Green-bordered pages. Gives off hydrogen fluoride.

## Slide 69: Protective Action Distance?
Small spill
At night
Notes: Table 1. Green-bordered pages. 0.2 miles.

## Slide 70: Container Stress & Behavior
E-18

## Slide 71: Container Stress & Behavior
Hazmats are released when container fails
  Failure can be minor or catastrophic
  Nature of failure determines potential harm
    Kingman BLEVE vs. Tokyo Sarin
E-18

## Slide 72: Hazmat Release Process
Stress on container
Container weakens & fails
Material released
Material disperses
E-18

## Slide 73: Hazmat Release Process
Hazard to you depends what step the process is on when you arrive!
E-18

## Slide 74: Types of Container Stress
Thermal
  Hot or cold
Mechanical
Chemical
E-18

## Slide 75: Evaluating Container Stress
Type of stress?
What will container do?
When will it do it?
E-18

## Slide 76: Action Planning for FRAs
Pay attention to container stress
Follow ERG recommendations
E-18

## Slide 77: Types of Container Failure
Catastrophic
Fracture
Puncture
Degradation
E-20

## Slide 78: Types of Product Dispersion
Instantaneous release
  Spreads in all directions
  Gases/vapors can ignite immediately
E-20

## Slide 79: Types of Product Dispersion
Rapid release
  Spreads downwind/downstream
E-20

## Slide 80: Types of Product Dispersion
Slow release
  Spreads slowly downwind/downstream
E-18
E-20

## Slide 81: BLEVE
Cause – Thermal stress on container
  Stress weakens container
  Container breeches
  Near-instantaneous release
E-20

## Slide 82: BLEVE
Hazards
  Flying debris
E-20

## Slide 83: BLEVE
Hazards
  Large fireball
E-20

## Slide 84: BLEVE
Timeframe
  Less than 10 minutes
E-20

## Slide 85: Rating Risks
Low
Moderate
High
Unacceptable
E-22

## Slide 86: Low Risk
Small quantities
Inert solid materials
Undamaged container
E-22

## Slide 87: Moderate Risk
Smaller quantities
Low vapor-pressure liquid materials
Undamaged/slightly damaged container
E-22

## Slide 88: High Risk
Large quantities/multiple containers
Low vapor-pressure liquids or gases
Slightly/moderately damaged container
E-22

## Slide 89: Unacceptable Hazmat Risk
Larger quantities and/or gas cylinders involved
High vapor-pressure liquids, gases, explosives and/or reactive materials
Visibly stressed container and/or flame impingement on a gas cylinder
E-22

## Slide 90: Unacceptable Hazmat Risk
An unacceptable risk here is:
E-22

## Slide 91: IDHA Complications
Many variables affect IDHA
May influence physical properties
E-24

## Slide 92: Variables & Modifying Conditions
Location can influence dispersion
  Stuff goes downhill
  Buildings can trap and/or redirect airborne contaminants
E-24

## Slide 93: Variables & Modifying Conditions
Time of day can affect:
  Evaporation rate
  Flammability
  Reactivity
E-24

## Slide 94: Variables & Modifying Conditions
Weather
  Gases/vapors will usually go downwind
  Vapor clouds can take longer to disperse in cold weather
E-24

## Slide 95: Variables & Modifying Conditions
Nature of materials
  Semi Bad Stuff or
  Bad Stuff or
  Really Bad Stuff
E-24

## Slide 96: Variables & Modifying Conditions
Type of Release
  Slow leak?
  Fast leak?
  Catastrophic leak?
E-24

## Slide 97: Variables & Modifying Conditions
Size of problem
  Bad stuff? How much?!?!?
E-24

## Slide 98: Variables & Modifying Conditions
Type, condition & behavior of container
E-24

## Slide 99: Reactivity & Combustion
Substances can react with
  Each other
  Air
  Water
E-24

## Slide 100: Reactivity & Combustion
Difficult to predict
ERG Green pages, Table 2 can help
E-24

## Slide 101: Bottom Line…
Same material
Different variables
Different response
E-24

## Slide 102: There Is No Cookbook
Use your head!
E-24

## Slide 103: Questions?