| Name: | Test: | Date: |
| --- | --- | --- |
| Federal Fire Department Test Certification |
| Certification | Ventilation with Chain Saw |

| Standard: demonstrate the ability to cut roof ventilation holes utilizing the gas-powered chain saw. Demonstrate proper chain saw maintenance. |
| --- |
| Steps required To Successfully Complete | Successfully Completed |
| 1. Wears full turnouts and SCBA. |  |
| 2. Secures chain saw and equipment necessary for evolution. Note: Firefighter should bring two saws and rubbish hook to roof prop. |  |
| 3. Properly starts chain saw prior to getting on roof prop. |  |
| 4. Knowledge of all controls and their location. |  |
| 5. Firefighter climbs ladder to roof prop with rubbish hook and sounds roof prior to being off ladder. |  |
| 6. Firefighter sounds roof while walking to area of roof to be ventilated |  |
| 7. Firefighter correctly passes back sounding tool to their non fire side and receives the chain saw to their fire side. |  |
| 8. Firefighter correctly explains the proper technique for cutting an Inspection hole, kerf cut, and smoke indicator hole |  |
| 9. Firefighter cuts a heat hole spanning no more than two rafters. Cuts shall be as follows: First cut is head cut, second cut is cut along rafter furthest from ladder, third cut is bottom cut, fourth cut is along rafter closest to the ladder. |  |
| 10. Firefighter correctly passes back chain saw to their fire side and receives Sounding tool to their non fire side. |  |
| 11. Firefighter correctly louvers heat hole with wind direction |  |
| 12. Firefighter simulates knocking out ceiling material with the D handle and verbalizes it is done next to the ceiling joist. |  |
| Successfully Completes | Yes: | No: |
| Comments: |  |  |
| Captain: |